Form 9.1 Installation checklist:  Demand/timed dosed pumps and siphons

Client name: 			 Reference #:

Permit(s) #:

Completed by: 		 Time:				 Date:

System type:		( Pump	( Siphon

1.	Control type:

( Piggyback		( Control panel	(  Siphon counter

a. 	Panel					( NA	( Yes	( No

Manufacturer:

Model:

( NEMA 4X Panel rating

Elapsed time meter				( NA	( Yes  	( No

Cycle counter				( NA	( Yes  	( No

b. 	Timer

Manufacturer:

Model:

c.	Telemetry             				( NA	( Yes  	( No

Manufacturer:

Model:

2. 	Pump							( NA	( Yes  	( No

a.	Pump manufacturer:

Model:

b.	Type of pump:    	(  Multi-stage  	(  Single-stage

(  Sewage  		(  Effluent		(  Grinder

c.	Pump specifications:

i.	Design flow rate:										 gpm

ii.	Design pressure (TDH):									 ft

iii.	Horsepower:										 hp

d.	Pump installed under access						( Yes  	( No

e.	Pump intake elevated:   	Height		 inches		( Yes  	( No

f.     Pump removal

(  Pull chain or rope installed  	(  Pump rails installed

(  Other:

g.	Pump vault flow rating: 										 gpm

3.    Siphon							( NA	( Yes  	( No

a.   	Siphon manufacturer:

Model:

b.   	Siphon capacity:										 gpm

c.   	Siphon installed under access 						( Yes  	( No

d.   	Siphon removable 							( Yes  	( No

e.   	Siphon cycle counter installed				( NA	( Yes  	( No

4.    Pump discharge assembly

a.	Quick disconnect 					( Installed

Type of disconnect:

Accessible from surface

b.	Isolation valve 				( Installed   	(  NA

Type of valve:

c.   Anti-siphon/air release device    	      	( Installed   	(  NA

(  Air release hole between check valve and pump discharge

(  Reversed check valve at high point in assembly

(  Spit tube

d.    Drainback allowed		                      			( Yes  	( No

e.	Inline filter     				( Installed    	(  NA

Manufacturer:

Model:

f.	Pressure gauge / port     				( Installed   	(  NA

g.	Sampling port					( Installed    	(  NA

5.	Supply lines and discharge pipes

a.	Air/vacuum release   					( Installed    	(  NA

b.	Thrust blocks 					( Installed    	(  NA

c.	Siphon discharge diameter greater than			( Yes	( No

or equal to trap diameter

Grade on siphon discharge pipe 	    			( Level	(  Sloping

6.	Water level sensors								(  NA

a. 	Type of water level sensor:  	(  Floats		(  Pressure transducer

(  Ohm probe  	(  Other:

b.    Sensor attachment

( Tethered to float tree

( Tethered to bracket on riser			(  Other:

c.	Sensor settings:

| Sensor number* | Function | Set at** | Secured |
| --- | --- | --- | --- |
|  |  | Inches | Datum |  |
| 1 |  |  |  | ( Yes ( No |
| 2 |  |  |  | ( Yes ( No |
| 3 |  |  |  | ( Yes ( No |
| 4 |  |  |  | ( Yes ( No |
| 5 |  |  |  | ( Yes ( No |

*Designate starting from bottom of tank.

**Measurements are taken from a fixed point (Datum) near the surface or bottom of float tree.

d.    (  Pump will be submerged at OFF elevation

7.	Wiring 		(  NA

a. 	Electrical service

( Single-phase 120V	( Single-phase 240V		( 3-phase 240/120V

( 3-phase 208/120V

b.    Wire gauge: 		     	( Adequate for distance

c.     (  Wire contained within conduit and junction boxes

Conduit sealed          	 ( Within panel  		(  Within dosing tank riser

Sealant used:

d.     (  Float wires color-coded:

| Sensor number* | Function | Color |
| --- | --- | --- |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |

e.	Connections completed by

(  Electrician        			(  Installer

(  Homeowner   				(  Other:

# Text boxes

Comments:

Comments: